## Slide 1: Stark broadening method of Hydrogen Balmer beta for low-density atmospheric pressure discharges
Faculty of Physics, University of Belgrade
N. Cvetanović,B . M. Obradović,
AsSpectro2022

## Slide 2
Measurement of electron density at Atmospheric pressure plasma
In recent years there has been a growing demand for measuring the electron density in atmospheric pressure discharges suitable for application. Such data is crucial for modeling and reactor optimization.
However, here measurement of plasma density using spectroscopic methods poses a difficult task, since all such plasma is of low to mid density. Therefore, the nonhydrogenic atomic lines spectra cannot be used and the only option are the hydrogen lines, mostly Balmer beta and gamma. Fortunately, in atmospheric pressure plasma hydrogen is always present in traces, and Balmer lines are strong enough to be employed, for example Cvetanović et al. 2018.
The Hβ line is commonly used to obtain electron density due to its advantages of strong Stark broadening dependence on electron density, and weak sensitivity to electron temperature. However, its broadening can only be applied in the case of considerably high electron density (>1020 m−3) making it difficult to apply to many types of low temperature plasma, N. Konjević et al. 2012. Using the classical Voight fit below this value may lead to significant error and uncertainty.

## Slide 3
Measurement of electron density at Atmospheric pressure plasma
Example of Balmer lines from atmospheric presure Ar plasma

## Slide 4
1016 cm-3
1014 cm-3

## Slide 5
Measurement of electron density at Atmospheric pressure plasma
A fine-structure fitting method must be applied to get more accurate results. This fitting method is based on assuming that the broadening mechanism of Hβ line also applies to the 7 fine-structure components
In the fine-structure fitting, Stark broadening is calculated by assigning a Voigt shape to each fine component. The overall profile is then analyzed by convoluting separate fine structure transitions of Hβ as line profiles, with relative line strengths and line shifts being the same as in the zero-field case. Due to the low plasma density, this may be taken as a valid assumption.
In other words, each fine-structure transition is assigned with its corresponding Doppler, Van der Waals, Stark broadening, and instrumental broadening so that the overall profile is obtained as a superposition of profiles.
In this approach, the same Stark width which is expected from theory for the entire line, is assigned to each fine-structure component. The fine-structure fitting can be used to improve the accuracy of electron density calculation close to the threshold of classical method, but above all for checking the validity of the obtained results for plasma density in the conditions when Van der Waals broadening is below the fine-structure limit of 0.05 nm.

## Slide 6
Applied in two experiments with atmospheric pressure helium discharges, Wang 2020. RF with bare and covered electrodes.